## Slide 1: Lecture 02: More on Memory and I/O Modules

## Slide 2: William Stallings Computer Organization and Architecture
Chapter 7
Input/Output

## Slide 3: Key Content
The function of Input/Output module
I/O addressing
Different I/O techniques
  Programmed
  Interrupt
  Direct Memory Access (DMA)

## Slide 4: Input/Output Problems
Wide variety of peripherals
  Different operation logic
  -> impractical for CPU to control all kinds of devices
  Speak different "languages"
    Delivering different amounts of data, e.g., serial/parallel
    At different speeds
    In different formats, e.g., analog/digital
  -> impractical for CPU to understand
  Slower than CPU and RAM
  -> impractical to directly connect devices with high-speed system bus
We need I/O modules (ports)!

## Slide 5: Input/Output Module
Interface to the CPU and Memory
Interface to one or more peripherals
It's like a bridge, an interpreter, a buffer, and …

## Slide 6: External Devices
Human readable
  Screen, printer, keyboard
Machine readable
  Monitoring and control
Communication
  Modem
  Network Interface Card (NIC)

## Slide 7: I/O Module Function
Control & Timing
CPU Communication
Device Communication
Data Buffering
Error Detection

## Slide 8: I/O Steps
For example, the control of the transfer of data from an external device to the processor
  CPU checks I/O module for device status
  I/O module returns the device status
  If the device is ready, CPU requests data transfer by means of a command to the I/O module
  I/O module gets a unit of data from device
  I/O module transfers the data to CPU
  Variations for output, DMA, etc.

## Slide 9: I/O Module Diagram
Data Register
Status/Control Register
External
Device
Interface
Logic
External
Device
Interface
Logic
Input
Output
Logic
Data
Lines
Address
Lines
control
Lines
Data
Status
Control
Data
Status
Control
Interface to Systems Bus
Interface to External Device

## Slide 10: I/O Module Design Decisions
Hide or reveal device properties to CPU
Support multiple or single device
Control device functions or leave for CPU

## Slide 11: Input Output Techniques
Programmed
Interrupt driven
Direct Memory Access (DMA)

## Slide 12: Programmed I/O
CPU executes a program that gives it direct control of the I/O operation
  Sensing device status
  Read/write commands to the I/O module
  Transferring data
CPU waits for I/O module to complete operation

## Slide 13: Programmed I/O - detail
CPU requests I/O operation
I/O module performs operation
I/O module sets status bits
CPU checks status bits periodically
I/O module does not inform CPU directly
I/O module does not interrupt CPU
CPU may wait or come back later (for example, with the help of time-sharing OS)

## Slide 14: I/O Commands
CPU issues address
  Identifies module (& device if >1 per module)
CPU issues command
  Control - telling module what to do
    e.g. spin up disk
  Test - check status
    e.g. power? Error?
  Read/Write
    Module transfers data via buffer from/to device

## Slide 15: Addressing I/O Devices
Under programmed I/O data transfer is very like memory access (from CPU viewpoint)
Each device is given a unique identifier
CPU commands contain the identifier (address) of the corresponding module (and device)

## Slide 16: Addressing Schemes Revisited
Memory mapped I/O
  Devices and memory share an address space
  I/O looks just like memory read/write
  No special commands for I/O
    Large selection of memory access commands available
Isolated I/O
  Separate address spaces
  Need I/O or memory select lines
  Special commands for I/O
    Limited set

## Slide 17: Problem with Programmed I/O?
Simple, but if CPU is faster,
it is a huge waste of CPU time

## Slide 18: Interrupt Driven I/O
Overcomes CPU waiting
No repeated CPU checking of device
I/O module interrupts when ready

## Slide 19: Interrupt Driven I/O Basic Operation
CPU requests I/O operation
I/O module performs operation while CPU does other work
I/O module informs CPU when something comes up by interrupting CPU
CPU deals with this event

## Slide 20: Handling an Interrupt: from a Protocol Perspective
A program called interrupt handler
Draw a protocol:
Which parties?
Interactions?
What’s interrupt?
New event needs CPU to handle first but CPU needs to go back to previous work after that
Notes: How can the CPU know which device is generating the interrupt? What is the new PC value?

## Slide 21: CPU Viewpoint
Issue read command
Do other work
Check for interrupt at the end of each instruction cycle
If interrupted:-
  Save context (registers)
  Process interrupt
    Fetch data & store
  Recover from the saved context

## Slide 22: Design Issues
How can CPU know which module is issuing the interrupt?
  when there are multiple devices connected to the system
How to locate the corresponding handler program when interrupted?
How do you deal with multiple interrupts?
  Possible for more than one devices to issue an interrupt simultaneously or in a row

## Slide 23: Identifying Interrupting Module (1)
Connect a dedicated line for each module
  Limits the number of devices
Software poll
  All devices share one common Interrupt Request line to interrupt CPU
  Once get an interrupt, CPU asks each module in turn
  CPU clears the interrupt request status of the module responsible

## Slide 24: Identifying Interrupting Module (2)
Daisy Chain or Hardware poll
  All devices share one common Interrupt Request line to interrupt CPU
  Interrupt Acknowledge signal is sent down a chain
Bus Master
  Module must claim the bus before it can raise interrupt
  e.g. PCI & SCSI
Interrupt controller
  8259

## Slide 25: Localizing Handler Programs
Using a general handler program
  CPU enters this handler every time it gets interrupted
  looks for the module responsible and gets the address of the corresponding handler program
Using interrupt vectors
  instead of using fixed locations, a handler program can be stored anywhere in memory
  a pointer is used to link to the handler program
  the address of the pointer is fixed and known to CPU
  such pointers are interrupt vectors
  Pros and cons?

## Slide 26: Dealing with Multiple Interrupts
  Set priorities for interrupts
  i.e., high-priority interrupts get served first
  Given a interrupt identification scheme, how to set priorities?
    Software and hardware polling, bus mastering
  Nesting of interrupts
    i.e., high-priority interrupts can further interrupt low-priority interrupts

## Slide 27: Problem with Programmed and Interrupt-driven I/O?
They both need the involvement of CPU.

## Slide 28: Direct Memory Access
Interrupt driven and programmed I/O require active CPU intervention
  Transfer rate is limited
  CPU is tied up
DMA is the answer

## Slide 29: DMA Function
Additional Module (hardware) on bus
DMA controller takes over from CPU for I/O

## Slide 30: DMA Operation
CPU tells DMA controller:-
  Read/Write
  Device address
  Starting address of memory block for data
  Amount of data to be transferred
CPU carries on with other work
DMA controller deals with transfer
DMA controller sends interrupt when finished

## Slide 31: DMA Transfer Cycle Stealing
In an instruction cycle, the processor may be suspended due to DMA operation
  CPU suspended just before it accesses bus
  DMA controller takes over bus for a cycle
  Transfer of one word of data
  Not an interrupt: CPU does not switch context
  Slows down CPU but not as much as CPU doing transfer

## Slide 32: DMA Configurations (1)
Single Bus, Detached DMA controller
Each transfer uses bus twice
  e.g., I/O to DMA then DMA to memory
For one transfer, CPU is suspended twice
CPU
DMA
Controller
I/O
Device
I/O
Device
Main
Memory

## Slide 33: DMA Configurations (2)
Single Bus, Integrated DMA controller
Controller may support >1 device
Each transfer uses bus once
  DMA to memory
For one transfer, CPU is suspended once
CPU
DMA
Controller
I/O
Device
I/O
Device
Main
Memory
DMA
Controller
I/O
Device

## Slide 34: DMA Configurations (3)
Separate I/O Bus
Bus supports all DMA enabled devices
Each transfer uses bus once
  DMA to memory
For one transfer, CPU is suspended once
CPU
DMA
Controller
I/O
Device
I/O
Device
Main
Memory
I/O
Device
I/O
Device

## Slide 35: Which way is the best?
Simplicity
Performance

## Slide 36: Assignment Two
Computer Organization and Architecture 8e by William Stallings
  Problem 7.8, 7.9, 7.10 (a, b)